## Slide 1: Experiment – 1 Instruction Set of 8086

## Slide 2: Instruction Set of 8086
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8086 has more than 20,000 instructions.

## Slide 3: Classification of Instruction Set
Data Transfer Instructions
Arithmetic Instructions
Bit Manipulation Instructions
Program Control / Transfer Instructions
String Instructions
Processor Control Instructions

## Slide 4: 1. Data Transfer Instructions
These instructions are used to transfer data from source to destination.
The operand can be a constant, memory location, register or I/O port address.

## Slide 5: Data Transfer Instructions (Conti..)
MOV Des, Src:
  Src operand can be register, memory location or immediate operand.
  Des can be register or memory operand.
  Both Src and Des cannot be memory location at the same time.
  E.g.:
    MOV CX, 037A H
    MOV AL, BL
    MOV BX, [0301 H]

## Slide 6: Data Transfer Instructions (Conti…)
PUSH Operand:
  It pushes the operand into top of stack.
  E.g.: PUSH BX
POP Des:
  It pops the operand from top of stack to Des.
  Des can be a general purpose register, segment register (except CS) or memory location.
  E.g.: POP AX

## Slide 7: Data Transfer Instructions (Conti..)
XCHG Des, Src:
  This instruction exchanges Src with Des.
  It cannot exchange two memory locations directly.
  E.g.: XCHG DX, AX

## Slide 8: Data Transfer Instructions (Conti…)
IN Accumulator, Port Address:
  It transfers the operand from specified port to accumulator register.
  E.g.: IN AX, 0028 H
OUT Port Address, Accumulator:
  It transfers the operand from accumulator to specified port.
  E.g.: OUT 0028 H, AX

## Slide 9: Data Transfer Instructions (Conti…)
LEA Register, Src:
  It loads a 16-bit register with the offset address of the data specified by the Src.
  E.g.: LEA BX, [DI]
    This instruction loads the contents of DI (offset) into the BX register.

## Slide 10: Data Transfer Instructions (Conti…)
LAHF:
  It copies the lower byte of flag register to AH.
SAHF:
  It copies the contents of AH to lower byte of flag register.
PUSHF:
  Pushes flag register to top of stack.
POPF:
  Pops the stack top to flag register.

## Slide 11: 2. Arithmetic Instructions
ADD Des, Src:
  It adds a byte to byte or a word to word.
  It effects AF, CF, OF, PF, SF, ZF flags.
  E.g.:
    ADD AL, 74H
    ADD DX, AX
    ADD AX, [BX]

## Slide 12: 2. Arithmetic Instructions ( Conti…)
ADC Des, Src:
  It adds the two operands with CF.
  It effects AF, CF, OF, PF, SF, ZF flags.
  E.g.:
    ADC AL, 74H
    ADC DX, AX
    ADC AX, [BX]

## Slide 13: Arithmetic Instructions ( Conti…)
SUB Des, Src:
  It subtracts a byte from byte or a word from word.
  It effects AF, CF, OF, PF, SF, ZF flags.
  For subtraction, CF acts as borrow flag.
  E.g.:
    SUB AL, 74H
    SUB DX, AX
    SUB AX, [BX]

## Slide 14: Arithmetic Instructions ( Conti…)
SBB Des, Src:
  It subtracts the two operands and also the borrow from the result.
  It effects AF, CF, OF, PF, SF, ZF flags.
  E.g.:
    SBB AL, 74H
    SBB DX, AX
    SBB AX, [BX]

## Slide 15: Arithmetic Instructions ( Conti…)
INC Src:
  It increments the byte or word by one.
  The operand can be a register or memory location.
  It effects AF, OF, PF, SF, ZF flags.
  CF is not effected.
  E.g.: INC AX

## Slide 16: Arithmetic Instructions ( Conti…)
DEC Src:
  It decrements the byte or word by one.
  The operand can be a register or memory location.
  It effects AF, OF, PF, SF, ZF flags.
  CF is not effected.
  E.g.: DEC AX

## Slide 17: Arithmetic Instructions ( Conti…)
AAA (ASCII Adjust after Addition):
  The data entered from the terminal is in ASCII format.
  In ASCII, 0 – 9 are represented by 30H – 39H.
  This instruction allows us to add the ASCII codes.
  This instruction does not have any operand.
Other ASCII Instructions:
  AAS (ASCII Adjust after Subtraction)
  AAM (ASCII Adjust after Multiplication)
  AAD (ASCII Adjust Before Division)

## Slide 18: Arithmetic Instructions ( Conti…)
DAA (Decimal Adjust after Addition)
  It is used to make sure that the result of adding two BCD numbers is adjusted to be a correct BCD number.
  It only works on AL register.
DAS (Decimal Adjust after Subtraction)
  It is used to make sure that the result of subtracting two BCD numbers is adjusted to be a correct BCD number.
  It only works on AL register.

## Slide 19: Arithmetic Instructions ( Conti…)
NEG Src:
  It creates 2’s complement of a given number.
  That means, it changes the sign of a number.

## Slide 20: Arithmetic Instructions ( Conti…)
CMP Des, Src:
  It compares two specified bytes or words.
  The Src and Des can be a constant, register or memory location.
  Both operands cannot be a memory location at the same time.
  The comparison is done simply by internally subtracting the source from destination.
  The value of source and destination does not change, but the flags are modified to indicate the result.

## Slide 21: Arithmetic Instructions ( Conti…)
MUL Src:
  It is an unsigned multiplication instruction.
  It multiplies two bytes to produce a word or two words to produce a double word.
  AX = AL * Src
  DX : AX = AX * Src
  This instruction assumes one of the operand in AL or AX.
  Src can be a register or memory location.
IMUL Src:
  It is a signed multiplication instruction.

## Slide 22: Arithmetic Instructions ( Conti…)
DIV Src:
  It is an unsigned division instruction.
  It divides word by byte or double word by word.
  The operand is stored in AX, divisor is Src and the result is stored as:
    AH = remainder AL = quotient
IDIV Src:
  It is a signed division instruction.

## Slide 23: Arithmetic Instructions ( Conti…)
CBW (Convert Byte to Word):
  This instruction converts byte in AL to word in AX.
  The conversion is done by extending the sign bit of AL throughout AH.
CWD (Convert Word to Double Word):
  This instruction converts word in AX to double word in DX : AX.
  The conversion is done by extending the sign bit of AX throughout DX.

## Slide 24: 3. Bit Manipulation Instructions
These instructions are used at the bit level.
These instructions can be used for:
  Testing a zero bit
  Set or reset a bit
  Shift bits across registers

## Slide 25: Bit Manipulation Instructions (Conti...)
NOT Src:
  It complements each bit of Src to produce 1’s complement of the specified operand.
  The operand can be a register or memory location.

## Slide 26: Bit Manipulation Instructions (Conti...)
AND Des, Src:
  It performs AND operation of Des and Src.
  Src can be immediate number, register or memory location.
  Des can be register or memory location.
  Both operands cannot be memory locations at the same time.
  CF and OF become zero after the operation.
  PF, SF and ZF are updated.

## Slide 27: Bit Manipulation Instructions (Conti...)
OR Des, Src:
  It performs OR operation of Des and Src.
  Src can be immediate number, register or memory location.
  Des can be register or memory location.
  Both operands cannot be memory locations at the same time.
  CF and OF become zero after the operation.
  PF, SF and ZF are updated.

## Slide 28: Bit Manipulation Instructions (Conti...)
XOR Des, Src:
  It performs XOR operation of Des and Src.
  Src can be immediate number, register or memory location.
  Des can be register or memory location.
  Both operands cannot be memory locations at the same time.
  CF and OF become zero after the operation.
  PF, SF and ZF are updated.

## Slide 29: Bit Manipulation Instructions (Conti...)
SHL Des, Count:
  It shift bits of byte or word left, by count.
  It puts zero(s) in LSBs.
  MSB is shifted into carry flag.
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.

## Slide 30: Bit Manipulation Instructions (Conti...)
SHR Des, Count:
  It shift bits of byte or word right, by count.
  It puts zero(s) in MSBs.
  LSB is shifted into carry flag.
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.

## Slide 31: Bit Manipulation Instructions (Conti...)
ROL Des, Count:
  It rotates bits of byte or word left, by count.
  MSB is transferred to LSB and also to CF.
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.

## Slide 32: Bit Manipulation Instructions (Conti...)
ROR Des, Count:
  It rotates bits of byte or word right, by count.
  LSB is transferred to MSB and also to CF.
  If the number of bits desired to be shifted is 1, then the immediate number 1 can be written in Count.
  However, if the number of bits to be shifted is more than 1, then the count is put in CL register.

## Slide 33: 4. Program Control / Transfer Instructions
These instructions cause change in the sequence of the execution of instruction.
This change can be through a condition or sometimes unconditional.
The conditions are represented by flags.

## Slide 34: Program Control / Transfer Instructions(Conti…)
CALL Des:
  This instruction is used to call a subroutine or function or procedure.
  The address of next instruction after CALL is saved onto stack.
RET:
  It returns the control from procedure to calling program.
  Every CALL instruction should have a RET.

## Slide 35: Program control / Transfer Instructions(Conti…)
Jump:
    Conditional Jump Instructions
    Conditional Jump Instructions
JMP Des:
  This instruction is used for unconditional jump from one place to another.
Jxx Des (Conditional Jump):
  All the conditional jumps follow some conditional statements or any instruction that affects the flag.

## Slide 36: Conditional Jump Table
Mnemonic | Meaning | Jump Condition
JA | Jump if Above | CF = 0 and ZF = 0
JAE | Jump if Above or Equal | CF = 0
JB | Jump if Below | CF = 1
JBE | Jump if Below or Equal | CF = 1 or ZF = 1
JC | Jump if Carry | CF = 1
JE | Jump if Equal | ZF = 1
JNC | Jump if Not Carry | CF = 0
JNE | Jump if Not Equal | ZF = 0
JNZ | Jump if Not Zero | ZF = 0
JPE | Jump if Parity Even | PF = 1
JPO | Jump if Parity Odd | PF = 0
JZ | Jump if Zero | ZF = 1

## Slide 37: Program control / Transfer Instructions(Conti…)
Loop Des:
  This is a looping instruction.
  The number of times looping is required is placed in the CX register.
  With each iteration, the contents of CX are decremented.
  ZF is checked whether to loop again or not.

## Slide 38: 5. String Instructions
String in assembly language is just a sequentially stored bytes or words.
There are very strong set of string instructions in 8086.
By using these string instructions, the size of the program is considerably reduced.

## Slide 39: String Instructions (Conti..)
CMPS Des, Src:
  It compares the string bytes or words.
SCAS String:
  It scans a string.
  It compares the String with byte in AL or with word in AX.

## Slide 40: String Instructions (Conti..)
MOVS / MOVSB / MOVSW:
  It causes moving of byte or word from one string to another.
  In this instruction, the source string is in Data Segment and destination string is in Extra Segment.
  SI and DI store the offset values for source and destination index.

## Slide 41: String Instructions (Conti..)
REP (Repeat):
  This is an instruction prefix.
  It causes the repetition of the instruction until CX becomes zero.
  E.g.: REP MOVSB STR1, STR2
    It copies byte by byte contents.
    REP repeats the operation MOVSB until CX becomes zero.

## Slide 42: 6. Processor Control Instructions
These instructions control the processor itself.
8086 allows to control certain control flags that:
  causes the processing in a certain direction
  processor synchronization if more than one microprocessor attached.

## Slide 43: Processor Control Instructions(Conti…)
STC:
  It sets the carry flag to 1.
CLC:
  It clears the carry flag to 0.
CMC:
  It complements the carry flag.

## Slide 44: Processor Control Instructions(Conti…)
STD:
  It sets the direction flag to 1.
  If it is set, string bytes are accessed from higher memory address to lower memory address.
CLD:
  It clears the direction flag to 0.
  If it is reset, the string bytes are accessed from lower memory address to higher memory address.

## Slide 45
Thank You