## Slide 1: Priority Interrupt Controller 8259

## Slide 2: Introduction
Need of Priority Interrupt Controller 8259
Connections of 8259 in 8086 system
Initialization
Interrupt Handling
Notes: Need: Only NMI,INTR, NMI power failure then only INTR left, insufficient, many sources of hardware interrupts, funneling-many interrupts to INTR
Connections, Initialization,IH - Agenda

## Slide 3: Connections
Working of INTR
When INTR received by 8086
8086-8259: two INTA* pulses
8259-8086: interrupt type
8086: intType * 4
Push flags
Clear IF and TF
Push return address
Get address of ISR from IVT
Load CS:IP

## Slide 4: Internal Block Diagram - 8259
D0-D7: CW, SW, IntType
IR0-IR7 --> INT high …
Int. Type
Int. Type = f(IR?,initNo.)
Funneling …
Notes: DR0 … 3 operations – CW from 8086 to 8259, status word from 8259 to 8086 and intType from 8259 to 8086
IR0 … Any line receiving interrupt causes INT output of 8259 high – connected to INTR 0f 8086 ie 808 interrupted so all the steps of previous slide
Int. Type … 8086 responds with two pulses on INTA* - during the second pulse – 8259 places interrupt type on Data Bus – first pulse details later
Int. Type depends upon IR input and the number that was sent to 8259 at the time of initialization
Funneling … Understand that how funneling is implemented

## Slide 5: Internal Block Diagram - 8259
Multiple requests on IRs
Interrupt Mask Register
Interrupt Request Register
In-Service Register
Notes: When multiple interrupts occur on IR lines of 8259 then priority is used for servicing. IR0 has the highest priority … IR7 the lowest priority .. In that order
Interrupt Mask Register … For every IR input one bt in this register .. We can mask IR input by setting the corresponding bit to 0 in this register
Interrupt Request Register - Every IR has one bit in this register … when interrupt occurs the corresponding bit in this register will be set to 1.
ISRegister … Every IR has one bit in this register … The interrupt that is currently being serviced – its corresponding bit is set

## Slide 6: Internal Block Diagram - 8259
Priority Resolver
Notes: Priority resolver – Suppose IR4 being serviced …and IR2 occurs .. 2nd bit in IRR is set .. IR2 has higher priority than IR4..So 8086 is interrupted..all the steps
Priority Resolver – Suppose IR4 being services .. IR6 occurs .. 6th bit in IRR is set .. After completing the IR4 then IR6 will be serviced

## Slide 7: Resolving Priority
STI – in main line code – INTR enabled
STI
EOI

## Slide 8: Resolving Priority
IR4 – not using STI – ie INTR not enabled

## Slide 9: 8259 in cascading mode

## Slide 10: 8259 in cascading mode

## Slide 11: 8259 in cascading mode

## Slide 12: 8259 in cascading mode

## Slide 13: 8259 in cascading mode

## Slide 14: Initializing 8259

## Slide 15: Initializing 8259

## Slide 16: Initializing 8259

## Slide 17: Initializing 8259

## Slide 18: Initializing 8259

## Slide 19: Initializing 8259
To find the system base address
Two addresses for 8259
The address1 is FF00H
The address2 is FF02H
A0:0 for internal address1
A0:1 for internal address2
CW: 00010011

## Slide 20: Initializing 8259

## Slide 21: Initializing 8259

## Slide 22: Operational Command Words (OCW)

## Slide 23: Operational Command Words (OCW)

## Slide 24: Operational Command Words (OCW)