## Slide 1: Reverse Breakdown Mechanism in PN - Junctions

## Slide 2: Reverse Breakdown Mechanisms
Zener breakdown occurs when the electric field is sufficiently high to pull an electron out of a covalent bond (to generate an electron-hole pair).
Avalanche breakdown occurs when electrons and holes gain sufficient kinetic energy (due to acceleration by the E-field) in-between scattering events to cause electron-hole pair generation upon colliding with the lattice.

## Slide 4: Avalanche Mechanism

## Slide 7: ZENER Diode as a Regulator

## Slide 8: Zener Regulator
The circuit is designed such that the diode always operates in the breakdown region and the voltage VZ across it remains fairly constant even though the current IZ through it vary considerably.
If the load IL should increase, the current IZ should decrease by the same percentage in order to maintain load current constant Is. This keeps the voltage drop across Rs constant and hence the output voltage.
If the input voltage should increase, the zener diode passes a larger current, that extra voltage is dropped across the resistance Rs. If input voltage falls, the current IZ falls such that VZ is constant.

## Slide 9
We now analyze the circuit to determine the proper choice of Rs. For the circuit shown in figure,
The current through the diode, iZ, is a minimum (IZ min) when the load current, iL is maximum (IL max) and the source voltage, vs is minimum (Vs min).
The current through the diode, iZ, is a maximum (IZ max) when the load current, iL, is minmum (iL min) and the source voltage vsis minimum(Vs max).